## Slide 1: COURSE TITLE CONSTRUCTION ENGINEERING AND MANAGEMENT
CHAPTER 11 (Week 11)
SPECIFICATION AND VALUATION
Lecture - 11
  Purpose of specification, Types of specification, Importance of specification, Valuation, Terms used in valuation, Methods of valuation
Er. Ishwar Adhikari
Associate Professor
Kathmandu Engineering College, Nepal

## Slide 2: Learning Objective
The main objective of this lecture is to understand about :
Purpose of specification.
  Types of specification.
  Importance of specification.
  Valuation.
  Terminologies in valuation.
  Methods of valuation.

## Slide 3: SPECIFICATION
The specification is the document where the level of intended quality is specified.
Specifications are clear concise descriptions of materials and workmanship including the methods of construction and precautions to be taken.
A specification is a specific description of a particular subject.
A specification definition is “written documentation describing the scope of work, any materials that are to be used, the methods of installation, and the quality of workmanship under contract.” [1]

## Slide 4: SPECIFICATION (Cont’d…)
An engineering specification contains detailed description of all workmanship and materials which are required to complete an engineering project in accordance with its drawings and details.
Specification specifies or describes the nature and class of the work, materials to be used in the work, workmanship etc. and is very important for the execution of work.
Specification should be clear and there should not be any ambiguity anywhere.
From the study of specification, one can easily understand the nature of the work and what the work shall be.

## Slide 5: SPECIFICATION (Cont’d…)
Specification depends on the nature of the work, purpose for which the work is required, strength of the materials, availability of the materials, quality of materials etc.
Drawings do not furnish the details of different items of work, the quantity of materials, proportion of mortar and workmanship, which are described in specifications.
Thus combinations of drawings and specifications define completely the structure. Drawings and specifications form important parts of contract document.
Specifications have two basic functions which are: Communicate and Compare.

## Slide 6: PURPOSE OF SPECIFICATION
To estimate the quantity and cost.
To specify the nature of the work.
To clarify any ambiguity.
To identity the quality of materials.
To identify the types of workmanship used.
To identify the material proportion.
To avoid the lengthy descriptions in bills of quantities and big captions on drawings and to supplements the information given in the drawings. [2]

## Slide 7: PURPOSE OF SPECIFICATION (Cont’d..)
It enables department, architect, engineers and contractor to define, procure and check the material’s quality as per specification.
To serve as guide to the bidders about the client’s/owner’s intended quality requirements and to arrive them at a fair price for the work involved. [2]
To serve as a part of contract documents between owner and the contractor limiting and describing their risks and responsibilities.
To serve as a guide for supervisors, engineers and fabricators regarding the methods of construction, fabrication, installation of equipment and materials.

## Slide 8: TYPES OF SPECIFICATION
Depending upon the purpose served, the specifications can be grouped as follows:
Contract Specification
(a) General/Brief Specification
(b) Detailed/Particular Specification
Standard Specification
Overall Performance Specification
Manufacturers Specification/Open Specification

## Slide 9: TYPES OF SPECIFICATION (Cont’d..)
Contract Specification
Contract specification is developed for a particular construction or project to accompany the working drawings.
(a) General/Brief Specification
This describes the nature of the purposed work, qualities of the materials and workmanship in general for the work as a whole. [2]
Gives the general description of the material, labor and types of equipment.
General specification gives general idea about whole work or structure and are useful for preparing the estimate.

## Slide 10: TYPES OF SPECIFICATION (Cont’d..)
  (b) Detailed/Particular Specification
The detailed specification is a detailed description and express the requirements in detail.
  It specifies the qualities and quantities of materials, the proportion of mortar, workmanship, the method of measurement.
  The detailed specification of different item of work are prepared separately and describes what the works should be and how they shall be executed and constructed.
  Physical, chemical and electrical tests if any requires for the finished work to ensure the desired strength or quality are specified in the detailed specification.

## Slide 11: TYPES OF SPECIFICATION (Cont’d..)
  The detailed specifications are expressed clearly as far as possible in the same sequence of order as the work carried out.
  These specification if prepared properly are very helpful for the supervisory staff for getting the work executed correctly and become an important part of contract agreement.
  This also specify the involvements and responsibility for auxiliary works, incidental damages etc. during execution of the original work.
  The method and duration of protection of finished works as required are specified in the detailed specification.

## Slide 12: TYPES OF SPECIFICATION (Cont’d..)
Standard Specification
This is generally prepared and published by national standard organizations which cover specific materials or group of materials used by a specific trade or a segment of the construction industry. [2]
A standard Specification is a set of the specifications for an item, material, component, system, or service that is defined precisely and established with the standardisation processes to be used for the business, engineering, procurement, construction, operation, and maintenance. [3]

## Slide 13: TYPES OF SPECIFICATION (Cont’d..)
Overall Performance Specification
This details in comprehensive but general terms, what the client is looking for.
Manufacturers Specification/Open Specification
Open specifications are specifications of products of manufacturers which state both physical and chemical properties and such other information of the product, but not description of workmanship to be achieved during construction.
The physical properties specify mainly the strength, weight, thickness or size and such other physical properties of product.

## Slide 14: SPECIFICATION WRITING
A specification becomes an essential contract management document which is used to ensure that the chosen supplier provides what is specified. [4]
It must therefore be clear and accurately define what is expected from a supplier regarding the outputs or the functional and performance requirements.
Specification serves as evidence in case of dispute. Most of the dispute occur only because of not properly explained/written specifications.
The general principles of specification writing are substantially the same regardless of the subject matter.

## Slide 15: SPECIFICATION WRITING (Cont’d…)
Specification language: Simple and clear. Same tense and repetition of a noun is preferable
Brief: as brief as possible. Standard article is specified by references and code numbers.
Fairness: fair to all parties. Proper sharing of risks
Expression: requirement of each and every item
Repetition of information is avoided to avoid the possibility of contradiction.
Standard size and patterns: commercial size should be specified as far as possible, unusual; dimensions should be avoidable.
Cross-references should be minimum as possible

## Slide 16: SPECIFICATION WRITING (Cont’d…)
Inclusion of proper paragraph
  specification of materials
  combinations of materials
  preliminary works prior to construction
  installation of materials
  test, if any
  clearing on completion
  mode of measurements
Quality of materials and workmanship should be specified
Nothing impossible to achieve and not intended to be enforced should be specified
While specifying the brand of materials options and choices should be given

## Slide 17: IMPORTANCE/ NECESSITY OF SPECIFICATION
Tender/contract document and agreement without specification is incomplete, baseless and invalid.
The cost of a unit quality of work is governed by its specification
To verify and check the strength of material for a work involved in a project
To specify the equipment, tools, and plants to be employed for works and thus enables to procure or hire
To procure the materials required for a project and to check the quality of materials
It serves as a guide for the site Engineer
Serves as an evidence in case of dispute
Changes in specification change the contract cost

## Slide 18: Specification of various items of works:
E /W in Excavation
  Clearing site
  Setting out
  Excavation
  Finish of trench
  Shoring
  Protection
  Disposal of excavated materials
  Dewatering
  Back Filling
  Measurement and Payment
Cement Concrete 1:2:4
  Materials
  Proportion
  Hand Mixing
  Machine mixing
  Slump
  Formwork
  Laying
  Curing
  Measurement
Gabions Work
  Materials
      Mild steel wire
      Stone
  Assembly
  Filling
  Measurement and Payment
Stone Masonry Work
  Materials: Cement, sand, water, stone
  Mortar Mix
  Mortar Preparation
  Preliminary work prior to laying
  Curing
  Measurement

## Slide 19: VALUATION
The process of determining the current worth of an asset or company is known as Valuation.
There are many techniques that can be used to determine value.
Valuation is the process of estimating what something is worth. Items that are usually valued are financial asset or liability.
The value of construction shall be based on the value of the work that is being performed.
The total value of work shall include materials and labor for which the permit is being sought for.

## Slide 20: VALUATION (Cont’d..)
In another way, valuation is an art of determining actual unbiased, legal and logical value of the property.
Property may be the land, building, both land and building, factory, machineries, jewelries and other engineering structures of various types.
The value of the property depends upon its structure, life span, location, maintenance etc.
Cost is the original cost and the original cost may be either construction cost or a purchase cost.
Value means the present (current) salable value of the property. Value may either less than or greater than the cost.

## Slide 21: VALUATION (Cont’d..)
Purpose of Valuation
  Buying and selling of property
  Taxation (local bodies tax , property tax and wealth tax)
  Rent fixation
  Security for loan or mortgage
  Compulsory acquisition
  For insurance
  To determine the court fee
  To prepare the balance sheet of company
  Partition of the property
  Reinstatement (to get the original value)

## Slide 22: VALUATION (Cont’d..)
Principle of valuation [2]
Costs depends upon supply and demand
Costs depends upon its design, specification and location
Costs varies with the purpose
Costs depends upon age and condition of property
Costs depends upon the psychology of the buyer and seller
Depends upon the present and future use of the property
Costs analysis must depends upon the statistical data

## Slide 23: VALUATION (Cont’d..)
Factors affecting the value of the property
Location (Land under urban and city area are expensive than in rural and semi-urban areas).
Climatic condition
Population census (Rate of migration and increase in population increases the demand for land and so cause in an increment of value) .
Supply and demand function (like other business, real estate business runs under the law of supply and demand)
Rate of interest (the transaction of real estate business increase when interest rate is decreased) .

## Slide 24: VALUATION (Cont’d..)
Topography (Mild slope and flat terrain land are of greater value in general than the sloppy and hill).
Rent restriction act (Government’s rent restriction act and its provisions affect the value of a property).
Abnormal condition (like insurgency, disaster, financial difficulties, etc. affects the value of a property).
Purpose (The same land for the agriculture purpose and industrial purpose differs).

## Slide 25: VALUATION (Cont’d..)
Qualification of Valuer’s
Planning, Designing and Construction works
Surveying and leveling
Estimating and quantity surveying
Knowledge on market rate of land
Rate of interest
Knowledge regarding rent act, and other prevailing acts and regulations
Building codes and bye-laws
Knowledge on Vastu Science
Report writing skills
And other required computer skills

## Slide 26: TERMS USED IN VALUATION
Gross income
Gross income is total income and includes all receipts from various sources. Outgoings are not deducted.
Net income
Net income is saving or the amounts left after deducting all outgoings from gross income.
Net income = Gross income – outgoings
Outgoings
Outgoings or the expenses which are required to be incurred to maintain the revenue of the property. These includes, taxes, repairs, management and collection charges, loss of rent and miscellaneous. [5]

## Slide 27: TERMS USED IN VALUATION (Cont’d…)
Book Value
The amount is shown in the account book after allowing depreciation.
The book value depends on the amount of depreciation allowed per year and will gradually reduce year to year.
At the end of the utility period, the book value will be equal to scrap value.
Book Value = original Cost- Depreciation
Salvage Value
It is the value of the property at the end of its utility period without being dismantled. In case of a machine, sale value at the end of its usual life span is the salvage value.

## Slide 28: TERMS USED IN VALUATION (Cont’d…)
Scrap Value
It is the value of the dismantled property (materials) after deducting labor charge to dismantle.
Distress value
Distress value is the value of the property at financial difficulties. It is always lower than the market value due to insufficient knowledge of property valuation.
Monopoly Value
Value of monopoly in nature and is always greater than the market value.
Assessed value
The value recorded for the municipal taxes.

## Slide 29: TERMS USED IN VALUATION (Cont’d…)
Obsolescence
It is the loss in the value of property due to an old design, out of fashion, out of date.
The obsolescence may be due to the reasons such as progress in arts, design, changes in fashion, trends, changes in design technique, planning ideas, etc.
Capital Cost
It is the total cost of construction including land or the original total amount required to possess a property.
It is the original cost and does not changes, while the value of a property is the present cost which may be calculated by methods of valuation.

## Slide 30: TERMS USED IN VALUATION (Cont’d…)
Capitalized Value
The capitalized value of a property is the amount of money whose annual interest at the highest prevailing rate of interest will be equal to the net income from the property. [6]
To determine the capitalized value of a property, it is required to know the net income from the property and the highest prevailing rate of interest.
Capitalized Value = Net income x year’s purchase
Year’s purchase is defined as the capital sum required to be invested in order to receive a net annual income as an annuity of $ 1 at a fixed rate of interest. [6]

## Slide 31: TERMS USED IN VALUATION (Cont’d…)
Sinking fund
It is the fund where a certain amount of gross rent is accumulated annually to reconstruct or to replace the property after useful life period.
14. Depreciation
Depreciation is the gradual reduction in the value of an asset due to wear and tear, usage, passage of time, obsolescence, depletion or inadequacy.[7]
The methods of calculating depreciation are straight line method, declining balance method, sinking fund method, SOYD method and MACRS method.

## Slide 32: METHODS OF VALUATION
Cost-based method of valuation
Depreciation method of valuation
Plinth area method
Rental method
Profit based method
Capital value comparison method
Development method

## Slide 33: METHODS OF VALUATION (Cont’d….)
Cost-based method of valuation
The cost approach method is based on the assumption that a potential buyer of a property should pay a price that is equal to the cost of constructing an equivalent building. [8]
This is the most accurate method of valuation in which detailed cost estimation of property is carried out by drawings and as-built structure.
Value of property = Value of building by detailed cost estimate – Total depreciation + Value of land
Total depreciation (D) = {cost of building – salvage value} * Age of building
Life of building

## Slide 34: METHODS OF VALUATION (Cont’d….)
Depreciation method of valuation
In this method, the depreciated value of the building is calculated.
Value of property = Depreciated value of building + Value of land
Where depreciated value of a building is calculated as,
Depreciated Value of Building = P { 1- d /100}n
Where
d = fixed rate of depreciation
P = Cost of building at present market rate = Total or Built-up area × Prevailing plinth area rate per meter square
n= Age of Building

## Slide 35: METHODS OF VALUATION (Cont’d….)
Plinth area method
In this method, the plinth area of the building is measured and calculated and plinth-area rate of a similar building in the locality is obtained by enquiry and cost is calculated. [9]
It is one of the popular method of valuation.
Value of property = Total plinth area (built-up area in m2)× prevailing plinth Area rate per m2 - Total depreciation + Value of land
Where, Total Depreciation (D) is calculated as,
D = (C – S)/n * age of building

## Slide 36: METHODS OF VALUATION (Cont’d….)
Rental method
In this method capitalized value of the property is calculated. It is used for the valuation of property which fetches the rent.
Value of property = Capitalized value
Capitalized value = Net rent × Years purchase
Net rent = Gross rent – outgoing (expenses)
Expenses: Repair, taxes, sinking fund, insurance, management and collection charges, loss of rent, etc.
Year's purchase =
ip = highest prevailing rate of interest in decimal
i = rate of interest for sinking fund in a decimal
n = life of a structure

## Slide 37: METHODS OF VALUATION (Cont’d….)
Profit based method
Used in the valuation of Hotel, Commercial complex, Cinema Hall, etc.
Value of property = Capitalized value of building + value of land
Capitalized value = Net income / profit × year's purchase
Net income = Gross income – outgoing
6. Capital value comparison Method of valuation
Use in land valuation by comparing the prevailing rate of land nearby vicinity.

## Slide 38: METHODS OF VALUATION (Cont’d….)
7. Development method
Development method of valuation is also used for properties or buildings which are required to be renovated by making alterations, additions, improvements etc. [9]
The value is calculated based on the anticipated net income generated from the building after renovation work is complete.
Developed value: Cost of land + Cost expenditure in development

## Slide 39: REFERENCES
[1] What Are Construction Specifications? By Grace Ellis, January 7, 2022, Digital Builder, accessed on 18th October 2023, https://constructionblog.autodesk.com/what-are-construction-specifications/#:~:text=Construction%20specifications%2C%20or%20specs%2C%20detail,quality%20of%20workmanship%20under%20contract.%E2%80%9D
[2] Text Book of Construction Management: S.K. Shrestha, Ram Kumar Shrestha and Subash Kumar Bhattarai, First Edition, Heritage Publisher and Distributors Pvt, Ltd, Kathmandu Nepal, 2014.
[3] The Project Definition, Standard Specification, posted on 21st December, 2015, accessed on 18th October 2023, https://www.theprojectdefinition.com/standard-specification/

## Slide 40: REFERENCES (Cont’d….)
[4] Specification writing – goods and services procurement guide, Find out how to develop and write specifications for goods and services procurement, accessed on 18th October 2023, https://www.buyingfor.vic.gov.au/specification-writing-goods-and-services-procurement-guide [5] Different types of outgoings required to maintain the revenue of the building, by study circle, June 14, 2022, accessed on 19th October 2023, https://cevnews.in/2022/06/different-types-of-outgoings-required-to-maintain-the-revenue-of-the-building/
[6] Capitalized Value and Year’s Purchase/Property Valuation System, August 9, 2010, accessed on 19th October 2023, https://www.civilprojectsonline.com/building-construction/capitalized-value-and-years-purchase-property-valuation-system/

## Slide 41: REFERENCES (Cont’d….)
[7] Engineering Economics and Costing : Dr. K.K. Patra & Dhiraj Bhattacharjee, First Edition, S. Chand and Company Ltd, 2013.
[8] Cost Approach (Real Estate), Written by CFI Team, accessed on 20th October 2023, https://corporatefinanceinstitute.com/resources/valuation/cost-approach-real-estate/
[9] Valuation of Building – Methods and Calculation of Valuation, Building Technology Guide, accessed on 20th October 2023, https://theconstructor.org/construction/valuation-of-building-methods-calculation/33091/